# Cisco IOS Image Naming Convention

Cisco Systems and other vendors who use Cisco IOS on routers, switches, and boards use a well-defined convention for naming software images. The convention identifies the platform or board for which the binary software is built, the package feature content of the image, and the area of memory used by the image at run-time. The image name follows a three part format, where:

### Cisco IOS Image Platforms (PPPP) Definition Identifiers

| as5200 | 5200 |
| --- | --- |
| cpa25 | CiscoPro 2500 |
| c1600 | 1600 |
| c2500 | 25xx,3xxx,5100, AO (11.2 and later only) |
| c2600 | 2600 Quake |
| c2900 | 2910, 2950 |
| c3620 | 3620 |
| c5rsfc | Catalyst 5000 series |
| c7000 | 7000,7010 (11.2 and later only) |
| c7200 | 7200 |
| gs7 | Gateway server (7000,7010) |
| gsr | Gigabit Switch Router (12000) |
| ls1010 | LightStream 1010 |
| ubr920 | Universal Broadband Router 920 |
| xx | 4000 |
| Igsetx | 2500 (media specific image that supports only Ethernet, token ring, and x.25) |

### Cisco IOS Image Feature Definition (FFFF) Feature Set Identifiers

| a | APPN |
| --- | --- |
| b | AppleTalk |
| Boot | boot image |
| c | CommServer lite (CiscoPro) |
| d2 | Reduced Desktop subset (SNMP, IP, IPX, ATALK, ARAP) |
| e | IPeXchange (prior to 11.3) StarPipes DB2 Access – Enables Cisco IOS to act as a “gateway” to all IBM DB2 products for downstream clients/servers in 11.3T |
| f | FRAD subset (SNMP, FR, PPP, SDLLC, STUN) |
| g | ISDN subset (SNMP, IP, Bridging, ISDN, PPP, IPX, AppleTalk) |
| h | For Malibu(2910), 8021D, switch functions, IP Host |
| i (not used for low end routers) |
| i | IP subset (SNMP, IP, Bridging, WAN, Remote Node, Terminal Services) |
| j | enterprise subset (formerly bpx, includes protocol translation) *** not used until 10.3 *** |
| k | kitchen sink (enterprise for high-end) (same as bx) (Not used after 10.3) |
| l | IPeXchange IPX, static routing, gateway |
| m | RMON (11.1 only) |
| n | IPX |
| o | Firewall (formerly IpeXchange Net Management) |
| p | Service Provider (IP RIP/IGRP/EIGRP/OSPF/BGP, CLNS ISIS/IGRP) |
| q | Async |
| r | IBM base option (SRB, SDLLC, STUN, DLSW, QLLC) - used with i, in, d |
| r2 | IBM variant for 1600 images |
| s | source route switch (SNMP, IP, Bridging, SRB) (10.x releases) 11.2(only) division by Platform c1600 (OSPF, IPMULTICAST, NHRP, NTP, NAT, RSVP, FRAME_RELAY_SVC) AT "s" images also have: (SMRP,ATIP,AURP) IPX "s" images also have: (NLSP,NHRP) c2500 (NAT, RMON, IBM, MMP, VPDN/L2F) |
| t | AIP w/ modified Ucode to connect to Teralink 1000 Data (11.2) |
| u | IP with VLAN RIP (Network Layer 3 Switching Software, rsrb, srt, srb, sr/tlb) |
| v | VIP and dual RSP (HSA) support |
| v2 | Voice V2D |
| w | Cisco Advantage ED train Feature Sets |
| x | X.25 in 11.1 and earlier releases. Also available in 12.0T on c800 series |
| y (used for low end routers) |
| y | IP variant (no Kerberos, Radius, NTP, OSPF, PIM, SMRP, NHRP...) (c1600) |
| z | Managed modems |
| 40 | 40 bit encryption |
| 56 | 56 bit encryption |
| 56i | 56 bit encryption with IPSEC |
| Obsolete |
| h | reduced desktop subset (SNMP, IP RIP/IGRP/EIGRP, Bridging, ISDN, PPP, IPX, AppleTalk) 1003/4 |

| Cisco IOS Execution Area |
| --- |
| F | Image runs in Flash |
| M | Image runs in RAM |
| R | Image runs in ROM |
| L | Image will be relocated at run time |
| Cisco IOS Image Compression Identifiers |
| Z | Image is Zip compressed (lower case z) |
| X | Image is Mzip compressed |
| W | Image is “Stac” compressed |

# Text boxes

Zipped Cisco IOS images are self-unzippable so that the users do not need to run extra commands to run

the software. As far as the user is concerned, they only need to get the image into the router flash or ROM.

At run-time, the image automatically unzips itself and relocates to the area of memory from where it is

intended to run. No further action is necessary from the system administrator.